## Slide 1: Types of Polymers

## Slide 2: Polymers are long and tangled
Remember, polymer molecules are long like spaghetti. Friction between noodles (or chains) slows down movement of a single chain
But with patience, you could slowly untangle all the noodles.
Notes: They are not chemically bonded
If you are patient enough you can unentangle them
The resistance to entanglement is what given polymers their interesting properties

## Slide 3: This type of polymer is called a thermoplastic
Thermoplastic
Chains entangle but do not link
Melts at high temperatures
Can dissolve in certain liquids
Stiff at use temperature
Notes: Thermoplastic: entangled but not chemically linked
  If you heat it up, the chains become more mobile and easily slow past each other
  Becomes something like a liquid
  Melts at high temperatures but it hardens back as soon as you cool them back to the original temperature
These polymers can also dissolve in certain liquids and become a solution just like when you dissolve salt in water
  You can no longer see the salt grains

## Slide 4: No dissolving or melting!
Create chemical linkages between the long chains.
One giant blob. Strands break instead of untangle.
Thermoset
Chains are chemically linked
Does not melt
Does not dissolve in any liquid (although is may swell)
Notes: What if you dont want it to dissolve or melt
When you overcook past and dont add any oil it congeals into a biiiig blob
We can do this with a polymer and now it is called a thermoset
A thermoset has chemical bonds (connections) among the chains
  Because of this, if you heat up the chains are not mobile anymore, so it does not become a liquid -> IT BUUURNS
  Also, it does not dissolve either
    It might even swell

## Slide 5: The main classes of polymers
Elastomer
Thermoset
Thermoplastic
Chains entangle but do not link
Chains are chemically linked
Chains are chemically linked
Does not melt
Swells in solvent
Melts
Dissolves in solvent
Notes: Those as the 2 main kinds of polymers, but there is another class: elastomer
  IT is pretty similar to a thermoset, but it is stretchy
  Both of them are crosslinked, so they will sell and not melt

## Slide 6: Hard, soft, or stretchy?
Elastomer
Thermoset
Thermoplastic
Chains entangle but do not link
Chains are chemically linked
Chains are chemically linked
Elastic
Rigid
Notes: Usually elastomers are elastic and the other 2 are stiffer

## Slide 7: Chemical structure determines properties
Elastomer
Thermoset
Thermoplastic
Chains entangle but do not link
Chains are chemically linked
Chains are chemically linked
Soft and elastic Tg < T
Hard and glassy when Tg > T
Glass transition temperature Tg
25°C
Notes: Elastomers are more flexible bc their Tg are lower than room temperature
Tg is the glass transition temperature
  It is the point at which the polymer goes from a state that is hard and brittle like glass (you can actually crack it like glass) to a soft/elastic state
  This is because the chains loose mobility and jam together below Tg. Above Tg, they gain mobility and the material becomes more flexible

## Slide 8: Chemical structure determines properties
Elastomer
Thermoset
Thermoplastic
Notes: Rubber bands: room temperature is above Tg -> very flexible and stretchy
Epoxy/Glue
  As soon as you pour it, the chains create crosslinks and room temperature is below Tg
  So, the material is stiffer
Plastic bottles
  Room temperature is below Tg, so they are stiff
  If you heat them up enough they melt and you can recycle them
  It is easier to recycle thermoplastics than the ones with permanent crosslinks

## Slide 9: How do looong molecules arrange themselves?
Notes: Usually in a material, the chains arrange themselves in a very particular way
Which way do you think the chains are arranged in a material? (MAke them pick one or another or both)

## Slide 10: What do polymers look like on the molecular level?
Amorphous
Crystalline
Semi-Crystalline
Notes: IF you picked messy: you are right in some cases! It is called amorphous
  Disorded, chaotically distributed
If you picked ordered: you are right in some cases! It is called crystalline
  This is not really a realistic case -> very hard to make it 100% crystalline
  This is because there are always some crystalline regions and amorphous regions
And if you said both: you’re also right -> semi-crystalline
  This is what happens a lot of times
The way the chains are arranged influence a lot their properties
The higher the crystallinity, the higher the Tg