## Slide 1: 3D Printing & Bio-based PLA
Notes: PLA: polylactic acid

## Slide 2: Types of 3D printing
Extrusion process
Less precise
More accessible
https://www.youtube.com/watch?v=P_DPHl_95MY
Stereolithography (SLA)
Filament
Light cure process
High precision
More technical
https://www.youtube.com/watch?v=kR7iDnrAxAU

## Slide 3: 3D printing workflow
Why 3D print?
Direct design to fabrication
Build on demand
Personalization
Computer-
aided design (CAD)
Slice and support (automated code)
Extrude or cure layer by layer
Final physical object

## Slide 4: 3D printing design considerations
Layer by layer
Base layer needs to stick to platform
Overhangs are challenging- require support
Personalization

## Slide 5: 3D printing filament
Different polymers for different properties and applications
Poly(lactic acid) is easy to print and biodegradable
  Melting temp is 170 - 180 °C
Other common filaments:
  ABS: strong and long-lasting, smells bad during printing
  PVA - water soluble supports

## Slide 6: PLA Lifecycle
Start from corn, tapioca roots, or sugarcane
Photosynthesis absorbs CO2
Raw materials
Fermentation
Polymerization
Biodegradation
Processing
Manufacturing

## Slide 7: Pros and cons
Derived from plant, not oil-based materials
Thermoplastic- can be recycled
Biodegrades in 1-3 months in commercial composting
Requires land and water to grow plants
Low glass transition means products soften and plastic degrades
Takes significantly longer to degrade in the wild (10’s of years in some cases)