## Slide 1: Fabric Properties

## Slide 2: Fabric properties depend on both fiber identity and knit
Tightly knit fibers reduce breathability
Tightly knit fibers have a greater contact with skin, increasing moisture wicking
The inherent chemical properties of the fiber impact water absorption, but coatings can obscure the effect.
Images of different types of knit patterns
Notes: https://www.rushordertees.com/blog/does-polyester-shrink/

## Slide 3: Desirable fabric properties
water-repellant
(hydrophobic)
stretchy
(elastic)
comfort
(heat retention, breathability)
Representative images for each fabric property

## Slide 4: Hydrophilicity from contact angle
hydrophilic
cotton
Super hydrophobic
Water-repellent coating
hydrophobic
polyester
Schematic image that shows how the measured contact angle relates to the hydro- classification of the material
Photos courtesy of Haley Beech

## Slide 5: Stretch from fiber and knit
Schultz, j., Polymer Material Science, 1974.
Semi-crystallinity lends strength and stretch to fiber
Stretch
Recover
Insert schematic image demonstrating stretch and recovery of semi-crystalline fibers
Insert schematic image demonstrating stretch and recovery of a knit material
Notes: https://refiberdesigns.com/blog/the-why-and-how-of-stretch-fabrics

## Slide 6: Breathability- key in a Brazilian summer
Skin
Micro
climate
Fabric
External
Environment
Breathability is the ability to transport moisture in the vapor state from an area of higher to lower humidity.
As your body heats up, the moisture vapors are absorbed by the fiber and released to the drier environment outside
Wool fiber can absorb and retain up to 30% of its own weight in moisture and still feel dry to the touch.
Representative schematic of breathable material and working principles
Notes: https://www.smartwool.com/discover/why-merino-wool/merino-wool-101.html

## Slide 7: Itchy? Try a finer fiber
The “itchiness” associated with some fabrics like wool is determined by the diameter of the fibers used.
Larger, broader fibers are less flexible and have less ability to bend, which results in a prick when pressed against the skin, causing the sensation of itch.
SEM image of fibers of various roughness
Notes: https://www.smartwool.com/discover/why-merino-wool/merino-wool-101.html